Name: Basant Raj Kadel
ID: 80117739

Lab-8:Connecting Disparate Networks using Static Routing on Cisco Routers
### 1. Objective To establish connectivity between two remote networks (192.168.1.0/24 and 192.168.2.0/24) by configuring static routes on two Cisco routers connected via a serial link (10.1.1.0/8).
### 2. Theory Routers use a routing table to determine the best path for forwarding packets to their destination. By default, a router only knows about networks that are directly connected to its interfaces.
### Static Routing: A network administrator manually configures the routing table, specifying the path for traffic to reach a specific network. This is done using the ip route command.
  - Use Case: Ideal for small networks with few paths, or for defining a specific exit path for traffic (e.g., a default route).
- Next-Hop Address: This is the IP address of the neighboring router's interface that a packet should be sent to in order to reach a remote network.
In this topology, Router1 knows about 192.168.39.0 and 10.1.39.0 but does not know how to reach 192.168.40.0 Similarly, Router2 needs to be told how to reach 192.168.39.0. Static routes provide this necessary information.
### 3. Diagram, Procedures, and Commands
#### Network Topology

Configuring Router1

Configuring Router2

Configuring the Static Routes
On Router1:

On Router2:
Configuring the PCs
- PC0 (in Network 1):
- Laptop0 (in Network 2)
### 4. Testing and Verification
1. Verifying Routing Tables:
  1. On each router, running show ip route. We should see a line with an S (Static) pointing to the remote network.
  2. On Router1:
  3. On Router2:
2. Testing Connectivity:
  1. Pinging the remote PC:
     ping 192.168.40.2

ping 192.168.39.2

  This proves the static routes are working correctly and the routers know how to forward packets to each other's networks.
### 5. Conclusion The lab successfully demonstrated the principle and configuration of static routing. Initially, the routers were only aware of their directly connected networks. By manually adding static routes using the ip route command, each router was informed of the path to the remote network. The successful ping from PC1 to PC2 confirmed that the routers could now correctly forward traffic between the disparate networks, enabling end-to-end connectivity. This method provides precise control over routing paths in a network.